## Slide 1
Respirator Fit Test
Orientation
April 2021
Notes: Welcome, opening remarks

## Slide 2: Housekeeping Details

## Slide 3: What is Fit Testing
  Process to identify the correct make, model and size of respiratory protection for workers
  Includes information to ensure workers understand the proper application, maintenance and pre-use testing for respiratory protection
  Includes practical demonstration that a worker can competently don and doff the respirator

## Slide 4: There is a Difference
Surgical/procedural mask
Most commonly used
Re-usable/disposable
Protects the patient/client and the worker
Less than 50% effective in protecting worker
Marked leakage around the borders of the mask
Respirator
Worn during air borne event
Re-usable/disposable
Protects worker from the patient/client and the environment
95% effective
Tight seal to the face
Must be fitted to the user’s face in order to achieve tight seal

## Slide 5: Legislation
Saskatchewan Occupational Health and Safety Regulations, 2020
3-11 Occupational health and safety program
7-1 Use of equipment required
7-3 Respiratory protective devices
21-8 Respiratory protective devices
CSA Standard Z94.4-18

## Slide 6: 3 Rights of Every Worker
Right to Know
Right to Participate
Right to Refuse – unusually dangerous work

## Slide 7: CSA Standard Z94.4-18
Sets the standards for workplace respiratory and fit testing programs
Sets out roles and responsibilities in a respiratory protection program

## Slide 8: CSA Standard Z94.4-18
Employer: has legislated duties
Program Administrator: ensures qualified personnel are assigned roles…
Supervisor: ensures training and testing are complete
Fit Tester: completes the fit testing including training component

## Slide 9: Fit Testing
Respirator User Screening Form must be completed prior to being fit tested
Then you will be fit tested
You have responsibilities following fit testing

## Slide 10: CSA Standard Z94.4-18
Users of Respirators are responsible to:
follow all written procedures – use, inspection, maintenance, storage
follow all requirements for respirator use
participate in refresher training and demonstrate ongoing competent use of your respiratory protective equipment
protect your own health and safety as well as that of fellow employees
inform your supervisor if concerns arise with equipment, process, procedures, health etc., which will affect the safe and efficient use of respiratory equipment
remove any respirator from service that you determine is defective and report it to your supervisor
perform user seal checks after donning a tight-fitting respirator.

## Slide 11: Respiratory Hazards
Oxygen deficient
Oxygen levels have decreased
Never enter suspected or confirmed oxygen depleted environments unless specifically trained to do so
Always check with your supervisor
Air borne contaminants
Biological
Dust
Vapours
Fumes
Fibers
Gases

## Slide 12: Respirators
Disposable – used once and thrown away
Elastomeric – re-usable; non-powered and powered
Both disposable and elastomeric respirators must be fit tested appropriately

## Slide 13: Hazards
OH&S Regulations 7-2, 3-11
Know the hazards associated with work tasks
Know how to protect yourself
Know signs/symptoms that might present themselves in cases of overexposure

## Slide 14: Respiratory Fit Test
Orientation for everyone
User screening form required
Fit tester will explain process
Following fit testing, know the size and make of respirator for you

## Slide 15: Frequency of fit testing
At least every 2 years unless:
Change in YOUR physical condition such as weight, broken nose
Change in respirator
Experience discomfort
Change in other Personal Protective Equipment

## Slide 16: Impact on respirator seal
Personal care items:
Be clean shaven
Severe scarring/acne
Facial piercings/heavy sweating
Make-up, face creams

## Slide 17: User Seal Checks
Negative:
Air purifying respirators and disposable respirators
Positive:
Respirators equipped with tight fitting face pieces

## Slide 18: Cleaning, Inspection, Maintenance and Storage
Cleaning
Sanitization
Inspection
Testing
Repair
Storage
Recordkeeping
Cautions/Limitations:
Know the cautions/limitations of the respirator fitted for you. This can be found on the packaging or on the instruction sheet from the manufacturer.

## Slide 19: Before being fit tested
ensure you do not eat, drink (except plain water), smoke, eat candy or chew gum for at least 15 minutes before the test is conducted
be clean shaven - facial hair will interfere with an effective respirator seal
present yourself in the same personal condition you would expect to be in when using the respirator:
wear your eye glasses/contact lenses/dentures that you would normally wear
have your hair in the manner you do when at work (e.g., hair bun)
include any personal protective equipment (such as eye protection/face shield)
understand that personal accessories, such as head coverings, garments, facial jewellery or other items shall not come between the skin and the sealing surface of the respirator, as well as make-up, creams and lotions may interfere.
Ensure you are on time for your fit testing.
It is an investment in your safety.

## Slide 20
Contact Us:
INSERT YOUR NAME/CONTACT NAMES
ENTER YOUR PHONE/EXTENTION
Be Aware – Be Healthy – Be Safe