## Slide 1
Respiratory Fit Testing
Train the Trainer
One part of an employer’s comprehensive safety program
with a focus on respiratory protection.
June 2022

## Slide 2: Housekeeping Details

## Slide 3: Welcome & Introduction
Welcome to Respiratory Fit Testing TTT
Successful completion of this program includes:
active involvement in discussion
return demonstration
Evaluation – pre session
Please follow along in the Fit Tester Protocols and Resources Binder

## Slide 4: Introductions
Your name
Where you work
Previous experience with fit testing

## Slide 5: What You Will Learn
Understanding Saskatchewan’s Occupational Health and Safety legislation and CSA standards pertaining to Fit testing
Overview of roles and responsibilities in a respiratory protection program
Hazard assessment
Selection of appropriate respirator
Respirator fit testing (qualitative and quantitative)
Orientation (self directed and facilitated)
Health Surveillance
Training
Program evaluation
Recordkeeping
Cleaning, inspection, maintenance and storage of respirators
Principles of Qualitative Fit Testing
Principles of Quantitative Fit Testing
Notes: As per slide

## Slide 6: SASWH Approved Fit Testers
Fit test trainers approved by SASWH have access to resources such as a PowerPoint for orientation and forms referenced in this material.
Visit www.saswh.ca and login/register with the following username and password (case sensitive)
  Username: RPP1
  Password: RPP2
Notes: All SASWH approved fit testers have access resources through our semi-secure site.
Go to SASWH.ca and login to show semi secure site

## Slide 7: Re-Approval
Fit testers require re-approval every 2 years by attending SASWH’s fit tester re-evaluation session.
A fit tester will be eligible for re-approval so long as they have fit tested/taught a minimum of 5 workers in the previous 2 years.
Notes: As per slide

## Slide 8: Legislation
Definition of “train”
Means to give information and explanation to a worker with respect to a particular subject matter and require a practical demonstration that the worker has acquired the knowledge or skill related to the subject-matter
Notes: Examples: When we do TLR training do we just show someone how to do a move and then say ok your good to go? No they have to show us they can safely perform that move in return.

## Slide 9: Supplies for Fit Testing
Orientation (either the presentation or worker’s can read the document)
Respirator user screening form
Respirator user tracking form
NIOSH approved respirators (elastomeric and/or disposable)
Mirror
Equipment/Supplies for the method of fit testing you are conducting (qualitative, or quantitative)
Safety data sheet for the sensitivity solution, and fit test solution (qualitative)
Safety data sheet for the alcohol solution (quantitative)
Water for participants of qualitative fit testing
Stickers/Wallet cards
Additional PPE that may be required based on the current situation
Notes: As per slide

## Slide 10: Risk Assessments
Self Risk Assessment
Consider if the fit tester is not able to perform the fit testing process on the day of training, or if a second fit tester is needed to assist
Assess communication skills to ensure participants understand the information fit testers are providing
Consider your own sensitivity to bitrex (when using qualitative method)
Is the fit tester equipped to handle an adverse reaction, who would the fit tester connect with if an adverse reaction happens, what is the emergency protocol
Notes: As per slide

## Slide 11: Risk Assessments
Equipment Risk Assessment
Ensure equipment has been maintained according to manufacturer guidelines (calibration, cleaning of nebulizers, humidifier for quantitative)
Check for loose classroom chair legs, table legs, frayed extension cords to ensure these items do no pose a risk of injury
Notes: As per slide

## Slide 12: Risk Assessments
Environment Risk Assessment
Consider loose tile/carpet, burnt out lightbulbs are repaired
Consider proximity to hazards/violence/excessive noise/odours/access/exits
For qualitative: rooms are to be well ventilated
For quantitative: a smaller room may be better for the count of air particulates
Notes: As per slide

## Slide 13: Reporting, Documenting, Communicating Identified Risks
Any defective/non-functioning equipment and/or items are not to be used during training
Report these risks, including how they were eliminated or managed according to the process for the site/area fit testing is being done
Notes: As per slide

## Slide 14: Three Rights of Workers
The Right to Know
  Every worker has a right to be informed about the hazards at work, trained to recognize those hazards, and trained to protected themselves from those hazards
The Right to Participate
  The occupational health committee (OHC) is the principal vehicle for worker participation in the workplace
The Right to Refuse
  A worker has the right to refuse unusually dangerous work
Notes: Explain 3 rights

## Slide 15: CSA Standard
CAN/CSA-Z94.4-18 Selection, use and care of respirators is the national standard of Canada. It provides guidelines for workplace respiratory fit testing programs
Notes: Describe CSA standard and how to gain access (through purchase or if SHA staff can access from library)

## Slide 16: CSA Standard
A respiratory protection program shall consist of the following components:
CAN/CSA-z94.4-18 | Aligned with OH&S Regulations, 2020
Roles and responsibilities: Clause 5 | General duties of employers: 3-1 General duties of workers: 3-2 Supervision of work: 3-6
Hazard assessment: Clause 6 | Exposure control plan: 6-22 Occupational Health and Safety program: 3-11
Respirator selection: clause 7 | Respiratory protective devices: 7-3, 21-8
Training: Clause 8 | General responsibilities: 7-2 General duties of employers: 21-1 Training of workers: 3-8
Respirator fit testing: Clause 9 | General responsibilities: 7-2 Respiratory protective devices: 7-2
Use of respirators: Clause 10 | General responsibilities: 7-2
Cleaning, inspection, maintenance and storage of respirators: Clause 11 | Exposure control plan: 6-22 General responsibilities: 7-2 Respiratory protective devices: 7-3 Inspection of respiratory protective devices: 7-4
Health surveillance: Clause 12 | Respiratory protective devices: 7-3
Program evaluation: Clause 13 | Exposure control plan: 6-22 General duties of employers: 21-1
Recordkeeping: Clause 14 | Occupational health and safety program: 3-11 Respiratory protective devices: 7-3
Notes: Go through chart, describe how CSA standard lines up with sections of the OHS Regulations

## Slide 17: Roles and Responsibilities
Employer (Clause 4.2.1): is responsible for preparing and implementing, in consultation with users, a written respiratory protection program including written procedures
Program Administrator (Clause 5.1): is responsible for the administration of the respiratory protection program
Respirator Users (Clause 5.2): once they have received their training, must ensure that they use and care for respirators in accordance with the written instructions and training received
Notes: As per slide

## Slide 18: Roles and Responsibilities
Supervisor (Clause 5.3): shall monitor respirator user to ensure that respiratory protection program requirements are being met, including user screening, training, fit testing and any medical assessment required are completed prior to assigning a user any task that requires the use of a respirator
Respirator Fit Tester (Clause 5.5) is the individual responsible for the hands on fit testing and training of respirator users. A fit tester MUST follow the protocols identified in the respiratory protection program.
Notes: As per slide

## Slide 19: Hazard Assessment
There are 2 main types of respiratory hazards in the workplace:
Oxygen deficient – Oxygen concentration is confirmed to be below 19.5%
Airborne Contaminants – the work area has levels of contamination which exceed workplace guidelines
  Airborne contaminants include:
    Biological hazards
    Dusts
    Mists
    Vapours
    Fumes
    Gases
    Fibers
Notes: Note: N95’s will not provide protection from all airborne contaminants on this list.

## Slide 20: NOTE
None of the respirators covered in SASWH’s fit testing session provide protection in oxygen depleted atmospheres
Air-supplying units are not part of this training and employees need specialized training to use air-supplying respirators
Employees should never be allowed to enter suspect or confirmed oxygen depleted environments
Always check with your supervisor regarding entering an oxygen deficient area
Notes: As per slide

## Slide 21: How to assess the hazards
CSA Z94.4-18, Section 6
6.1 General: a hazard and risk assessment shall be performed by a qualified person (or persons) to determine the respiratory hazards present and to assist in the selection of an appropriate respirator where required
Notes: As per slide

## Slide 22: Selection of Appropriate Respirator
Regardless of the respirator chosen, ensure it is NIOSH approved. For healthcare, the respirator must be healthcare specific (e.g. fluid resistant)
Types of respirators:
  Atmosphere-supplying respirators (SCBA, airline, multifunctional)
  Air purifying respirators, non-powered (APR) and powered (PAPR)
  Combined respirator (a configuration incorporating both atmosphere-supplying and air purifying
  Escape-only respirators (atmosphere supplying or air purifying
Notes: Note: 3M8210 can only be used with a face shield as they are not fluid resistant
We are only dealing with Air Purifying respirators

## Slide 23: Styles of APRs
There are several styles of air purifying respirators:
Non-powered air purifying
  Disposable respirators
    Fairly inexpensive
    Marked single use
    Made of cloth-like fibers and cannot be washed and reused
    N95 and N100 fall in this category
  Half-face elastomeric respirator
  Full face elastomeric respirator
Powered air purifying
  Tight seal which requires fit testing
  Loose hood does not require fit testing
Notes: The elastomeric respirators:
Reusable
Must be cleaned and maintained
Different types of cartridges
Must be NIOSH approved
Cartridges are replaceable
Powered air purifying: there are fans in them that move the air around inside the respirator, usually full –face respirators that have to be worn for a long time. (think grey’s anatomy during the covid season)
Cartridges for the PAPR and Elastomeric Respirators can be for different hazards such as particulates, gas and vapour, and multifunctional

## Slide 24: Particulate Respirator Rating
N95: filters out 95% if 0.3 micron sized particles in the atmosphere
N99: filters out 99% of 0.3 micron sized particles in the atmosphere
N100: Filters out 99.7% of 0.3 micron sized particles in the atmosphere
N: stands for not resistant to oil
R: stand for resistant to oil
P suitable for any particulate and oily atmosphere (P100 filters out 99.9% of 0.3 micron particles in the atmosphere)
Notes: As per slide

## Slide 25: Respirator Fit Testing
Once the hazard assessment has been completed, hazards have been recognized, and equipment has been chosen, now we conduct the fit testing
Notes: As per slide

## Slide 26: Respirator Fit Testing
In order to be competent, fit testers must be qualified through training and experience to conduct the appropriate tests that will ensure users are protected from hazards during respirator use.
Fit testers will be responsible to maintain and create, if necessary, records of fit testing done.
Notes: As per slide

## Slide 27: Fit Testing
The fit testers shall be competent in the applicable fit test methods and be able to verify a user’s ability to obtain an effective respirator seal, comfort, and a fit for a tight-fitting respirator.
The fit tester shall also be able to manage the overall fit testing process, including the transition between sensitivity screening and fit testing where applicable, interpret test results, and document user, respirator and instrument performance.
Notes: As per slide

## Slide 28: Limitations
Training on the use of a respirator shall include the limitations of the respiratory protection device.
Limitations are the restrictions, cautions, warning and prohibitions, imposed by manufacturers, testing and certification agencies, authorities having jurisdiction, and employers on the use, care, and maintenance of the respirator.
*The packaging on the respirator box or an informational insert from the manufacturer would indicate the cautions/limitations of that specific respirator
Notes: The packaging on the respirator box or an informational insert from the manufacturer would indicate the cautions/limitations of that specific respirator.

## Slide 29: Provision of training
Training shall be provided by a qualified person or persons with a practical understanding of the respiratory protection program roles, responsibilities, and requirements and the ability to coordinate the multiple training requirements of the program.
Trainers shall themselves be capable of demonstrating the care and practical use elements prescribed in Clause 8.1.6.
Notes: As per slide

## Slide 30: Respirator Fit Testing
The purpose of a qualitative or quantitative fit test is to verify a user’s ability to obtain an effective seal and an acceptably comfortable fit for a selected tight-fitting respirator.
The fit test process also verifies that a user is able to demonstrate the required level of competency in donning and doffing the respirator, as well as inspecting it and performing a user seal check.
Notes: As per slide

## Slide 31: Respirator Fit Testing
No person shall use or be assigned to use a tight-fitting respirator until a satisfactory fit has been verified by a qualitative or quantitative fit test.
Notes: As per slide

## Slide 32: Respirator Fit Testing
The fit test shall be used to verify the selection of the specific make, model, and size of a tight-fitting respirator for individual users.
A sufficient variety of respirators shall be provided to ensure that each user has an opportunity to obtain a satisfactory fit because no single make, model, or size can be expected to fit all persons.
The fit tester shall not force fit a respirator being fit tested.
Note: Force fitting is the practice of repeating a failed fit test with the same respirator by redonning or otherwise adjusting it (e.g., overtightening the straps) until a fit test pass is finally obtained. The user may adjust the respirator, but comfort should be maintained. Offering a reasonable array of respirator types and sizes should eliminate the inclination to force fit.
Notes: As per slide

## Slide 33: Respirator Fit Testing
Individuals who are unwilling or otherwise unable to comply with the interference-free requirement, or who are unable to obtain an acceptable fit, shall be prohibited from using a tightfitting respirator.
Fit testers shall follow the requirements of the program and shall not perform a fit test if they observe that the person is not free from interference where the respirator seals to the skin of the face or neck. In such cases, the fit tester shall notify the program administrator.
Notes: As per slide

## Slide 34: Respirator Interference Concerns
Facial hair: Individuals shall present themselves for fit testing free from interference of hair where the respirator seals to the skin of the face or neck.
Although the rate of hair growth varies among individuals, for many, this requires being clean-shaven within the previous 24 or preferably 12 h to ensure that hair neither infringes on the sealing surface of the respirator nor interferes with valve or respirator function.
Notes: As per slide

## Slide 35: Respirator Interference Concerns
Personal conditions: Individuals shall present themselves for fit testing in the same personal condition they would expect to be in when using the respirator.
This includes hair styles (e.g., hair buns) and wearing or not wearing dentures, eyeglasses, or contact lenses.
Notes: As per slide

## Slide 36: Respirator Interference Concerns
Personal effects or accessories: Individuals shall present themselves for fit testing in such a way that personal accessories such as head coverings, garments, facial jewelry, or other items shall not come between the skin and the sealing surface of the respirator.
Note: Such accessories can impair respirator effectiveness by interfering with valve function, respirator adjustability, and proper secure positioning.
Makeup, creams, or lotions can also interfere with effective respirator function.
Notes: As per slide

## Slide 37: Respirator Interference Concerns
Personal protective equipment (PPE) integration: When PPE such as eye, face, head, or hearing protectors or protective garments are required to be worn during respirator use, they shall be worn during respirator fit testing to ensure that the respirator seal is not compromised.
Notes: As per slide

## Slide 38: Qualitative Fit Testing (QLFT)
Qualitative fit testing shall be conducted in accordance with one of the procedures described in Annex B.
Only QLFT methods that are appropriate for the respirator as referenced in Table 3 of the CSA standard shall be used.
QLFT shall not be used for SCBA and multi-functional SCBA airline applications.
Notes: As per slide

## Slide 39: Quantitative Fit Testing (QNFT)
Quantitative fit testing shall be conducted in accordance with one of the procedures described in Annex C.
Only QNFT methods that are appropriate for the respirator as referenced in Table 4 of the CSA standard shall be used.

## Slide 40: Health Surveillance
Prior to fit testing and respirator use, the program administrator shall ensure that documentation is completed that confirms that individuals are free from any physiological or psychological condition that could preclude them from being fit tested on or using the selected respirator.
All health information shall be treated as medically confidential.
Notes: Talk SASWH Screening form

## Slide 41: Recordkeeping
General: The program administrator shall ensure that appropriate records are kept of all respiratory protection program activities as required by applicable legislation, employer policy, or as outlined in this Standard.
Recordkeeping should include documentation on:
the individuals fulfilling the roles and responsibilities of the program, including corresponding with users, qualified persons, and regulators
hazard assessment, including periodic monitoring of the workplace atmosphere
selection of the appropriate respirator
training
respirator facial fit
cleaning, maintenance, and storage of respirators
health surveillance of respirator users; and
program evaluation (see Clause 13).
Note: Records should be maintained for the duration of employment of the person trained or for a minimum of 10 years
Notes: Should the respiratory hazards change, the respirator selection process shall be repeated and
documented.

## Slide 42: Records of Respirator Fit Testing
Fit test records shall be retained for respirator users and shall meet all the following requirements:
the name of the person tested;
the date of the tests;
the specific make, model, and size of respirator;
the type of fit test method and test agent used;
pass/fail criteria for the fit test;
a list of additional PPE worn during the fit test;
notes on restrictions related to facial hair, use of dentures and corrective eyewear, or any particular fitting difficulties such as unusual facial features or use of facial jewelry or cosmetics;
the name of the person conducting the fit test;
result of comfort assessment steps criteria, through movements, observation, and scoring (e.g., 0,1,2,3);
further comfort assessment through the validation questions (see comfort assessment steps in Clauses B.2.3 and C.2.3 and in the example fit testing record form in Annex R);
documentation of the individual user’s competency, including pre-use inspection of the facepiece, donning and doffing and user seal checks, and corresponding fit test results;
documentation of any unsuccessful fit test and nature/cause(s) for the failure; and
documentation of the maintenance, calibration, and repair of fit test equipment
Notes: SASWH has developed and offers a Respirator Fit Test Documentation form that aligns with the
current CSA Standard (see Forms tab).

## Slide 43: Negative and Positive User Seal Checks
Several styles of respirators should be available for the test procedure.
Candidates will be given time to select a respirator that gives them a good positive and negative user seal check prior to the test.
Notes: As per slide

## Slide 44: Negative Pressure User Seal Check (elastomeric)
A negative-pressure user seal check can be conducted on air-purifying respirators and
atmosphere- supplying respirators equipped with tight-fitting facepieces.
This check can be difficult or impossible to conduct on respirators incorporating air-purifying elements that do not allow the inhalation inlets to be temporarily sealed.
Notes: As per slide

## Slide 45: Negative Pressure User Seal Check (elastomeric)
The procedure for conducting the negative-pressure user seal check shall be as follows:
The user seal check consists of closing off the inlet opening(s) of the respirator air-purifying elements so that upon inhalation, passage of air into the facepiece will not occur. In the case of atmosphere-supplying respirators, the user seal check consists of closing off the air supply hose.
To avoid possible disruption of the facial seal, a non-permeable, flexible plastic wrap may be used to seal the air inlets instead of attempting to maintain a seal with the hands.
The user shall inhale gently and hold a breath for at least 5 s. The facepiece will collapse slightly on the face and shall remain collapsed while the breath is held.
During this period, the facepiece shall not be disturbed by the user attempting to maintain a seal on the inlet opening of the air-purifying elements.
If the facepiece remains collapsed while a breath is being held, the user seal check is successful.
If the facepiece does not remain collapsed while a breath is being held, the user shall verify that nothing obstructs the sealing surface, adjust the facepiece and harness, and repeat the user seal check.
If the facepiece still does not remain collapsed while a breath is being held, then the user shall remove the respirator, inspect the components for the cause of the leakage, correct any problems discovered, or obtain a replacement respirator and repeat the user seal check.
Users shall not use a respirator for which a user seal check cannot be completed successfully.
Notes: As per slide – demonstrate seal checks on elastomeric respirator

## Slide 46: Positive Pressure User Seal Check (elastomeric)
A positive-pressure user seal check can be conducted on respirators equipped with tightfitting facepieces that contain both inhalation and exhalation valve
Notes: As per slide

## Slide 47: Positive Pressure User Seal Check (elastomeric)
The procedure for conducting the positive-pressure user seal check shall be as follows:
Don the respirator facepiece, closing off the exhalation valve or breathing tube, or both, and exhaling gently. Note: For some respirators, the positive-pressure user seal check requires that the exhalation valve cover be removed, then replaced following completion of the user seal check.
During this period, the facepiece shall not be disturbed by the user attempting to maintain a seal on the exhalation valve.
If a slight positive pressure can be maintained inside the facepiece without detection of any outward leakage of air, the user seal check is successful.
If a slight positive pressure cannot be maintained inside the facepiece for 5 s, the user shall verify that nothing obstructs the sealing surface, adjust the facepiece and harness, and repeat the user seal check.
If a slight positive pressure still cannot be maintained inside the facepiece, the user shall remove the respirator, inspect the components for the cause of the leakage, correct any problems discovered, or obtain a replacement respirator and repeat the user seal check.
Users shall not use a respirator for which a user seal check cannot be completed successfully.
Notes: As per slide – Demonstrate seal check on elsatomeric

## Slide 48: Negative and Positive Pressure User Seal Checks for Disposable Respirators
The following procedures are provided as examples once the respirator is properly donned.
Notes: As per slide

## Slide 49: Negative Pressure User Seal Check for Disposable Respirators
During a negative pressure user seal check, the respirator user inhales sharply while blocking the paths for air to enter the facepiece.
A successful check is when the facepiece collapses slightly under the negative pressure that is created with this procedure.
To conduct a negative pressure user seal check, the respirator user covers the filter surface with their hands as much as possible and then inhales. The facepiece should collapse on the users face and they should not feel air passing between their face and the facepiece.
Notes: As per slide – demonstrate on a disposable respirator

## Slide 50: Positive Pressure User Seal Check for Disposable Respirators
During a positive pressure user seal check, the respirator user exhales gently while blocking the paths for air to exit the facepiece.
A successful check is when the facepiece is slightly pressurized before increased pressure causes outward leakage.
To conduct a positive pressure user seal check, the respirator user exhales gently into the facepiece. The face fit is considered satisfactory if a slight positive pressure is being built up inside the facepiece without any evidence of outward leakage of air at the seal. Examples of such evidence would be the feeling of air movement on their face along the seal of the facepiece, fogging of their glasses, or a lack of pressure being built up inside the facepiece.
Notes: As per slide – demonstrate with a disposable respirator

## Slide 51: Negative and Positive Pressure User Seal Checks for Disposable Respirators
In either seal check, if air leaks around the nose, the respirator user uses both hands to readjust
the nosepiece by placing fingertips at the top of the metal nose clip. Slide fingertips down both sides of the metal strip to more efficiently mold the nose area to the shape of your nose. Readjust the straps along the sides of head until a proper seal is achieved. Repeat the seal checks.
Notes: Not every respirator can be checked using both positive and negative pressure. Refer to the
manufacturer’s instructions for conducting user seal checks on any specific respirator. This
information can be found on the box or individual respirator packaging.
If users cannot achieve a proper seal due to air leakage, they may need to be fit tested for a different respirator model or size.

## Slide 52: Qualitative Respirator Fit Tests (QLFT)
Acceptable QLFT methods: The following QLFT methods shall be acceptable:
QLFT using isoamyl acetate (banana oil) as a challenge agent in a test chamber following threshold screening, with non-detection of its odour by a test subject wearing a respirator serving as an indication of acceptable fit;
QLFT using saccharin solution aerosol as a challenge agent in a test chamber following threshold screening, with non-detection of its sweet taste by a test subject wearing a respirator serving as an indication of acceptable fit;
QLFT using bitter aerosol (denatonium benzoate) as a challenge agent in a test chamber following threshold screening, with non-detection of its bitter taste by a test subject wearing a respirator serving as an indication of acceptable fit; and
QLFT using irritant smoke (stannic chloride) as a challenge agent following threshold screening, with non-detection of it by a test subject wearing a respirator serving as an indication of acceptable fit.
Notes: Refer to the manufacturer’s SDS for appropriate handling and disposal procedures for the
challenge agents.

## Slide 53: Qualitative Respirator Fit Tests (QLFT)
Introduction of QLFT to respirator users: The person conducting the QLFT shall provide the test subject with an introduction to QLFT. In this introduction, the fit tester shall
explain what the QLFT procedure is, why it is required, and the importance of using a respirator that provides an effective, reproducible face-to-facepiece seal;
explain why the test is important, in order to convince the test subject to co-operate fully in the QLFT;
describe the challenge agent used in the QLFT and how to identify it;
describe how the test subject selects a properly fitting and comfortable respirator from those that are appropriate to the application;
explain that the respirator is equipped with the appropriate filters or chemical cartridges for the challenge agent being used;
explain that the test subject is required to successfully complete the positive- or negative-pressure user seal check with the selected respirator without physical or verbal assistance prior to proceeding with the QLF
explain that the test subject is required to don the respirator properly, without physical or verbal assistance, in accordance with the manufacturer’s instructions;
explain that the test subject is required, during the QLFT, to wear other PPE that he/she could be required to use in the workplace and that could affect the face-to-facepiece seal;
describe the QLFT exercises and how to perform them during the QLFT;
explain why it is important to use, in the workplace, the specific brand, model, and size of facepiece that is used to pass the QLFT; and
emphasize that the user must always inspect a respirator before using it to ensure that it is in proper working condition.
Notes: As per slide

## Slide 54: Qualitative Respirator Fit Tests (QLFT)
Comfort assessment conditions and criteria: Assessment of comfort and appropriateness of fit shall include the fit tester confirming through observation that the following conditions and criteria are met:
proper placement of the chin in its resting space;
proper fit and position of the facepiece on the nose (if a half-facepiece) or nose cup on the nose (if a full-facepiece);
position of the eyes within the facepiece lens to allow the best peripheral vision (if a fullfacepiece)
optimal strap tension (not too loose or too tight) and positioning;
accommodation of spectacles (lens inserts in a full facepiece) or eye protection (with a half- facepiece), without adversely affecting face-to-facepiece seal;
intelligible speech without an obvious break in the face-to-facepiece seal;
stability, against tendency for a facepiece to slip, create excessive pressure or break the seal, for example in the presence of movement or contact with other integrating PPE or accessories;
full contact of the sealing surface of the facepiece to the face;
proper positioning of additional integrating equipment (i.e., PPE) for function;
successful seal check, followed by
  sufficient time allowed (at least 5 min) for assessment of comfort in relation to the face-to- facepiece seal, strap tension, or other pressure points resulting from integrating PPE if worn, including corrective lens inserts, safety glasses, hoods, helmets etc.; and subsequently
  the wearer’s verbal confirmation of adequate comfort (see Clause B.2.3.5); and
repeated successful user seal check.
Notes: Note: Respirator comfort is an important factor in wearer acceptance. Respirators with greater
wearer acceptance are more likely to be worn appropriately. The selection should be based on
comfort and results of user seal checks, as well as personal preferences. Various factors that
influence wearer acceptance include breathing resistance, impairment of vision, impairment of
communications, and respirator weight.

## Slide 55: Qualitative Respirator Fit Tests (QLFT)
Comfort assessment movements: Throughout the process of assessing comfort that meets the criteria above, and after the waiting period, the wearer should perform the following movements for 3 to 5 s:
Nod head up and down.
Tilt head with left ear touching left shoulder and then right ear touching right shoulder.
Turn head from one side to the other.
Shake head twice vigorously.
Perform facial expressions: open and close mouth as if speaking, move the jaw left to right, up and down, smile, frown.
Notes: As per slide

## Slide 56: Qualitative Respirator Fit Tests (QLFT)
Comfort assessment scoring: The wearer shall be asked to score the facepiece according to the following criteria:
  0 - No issues
  1 - Discomfort that can be ignored
  2 - Some discomfort but still able to function
  3 - UNACCEPTABLE discomfort - not bearable
a) A score of 2 should prompt the fit tester to initiate a new redonning or repositioning or to
use an alternative respirator option.
b) A score of 3 shall result in rejection of the respirator worn. If the appropriate facepiece
for the application cannot be found, a protective alternative shall be made available
within the scope of the RPP. A small percentage of users will not be able to use any
tight-fitting facepiece.
Notes:
1) See Clause: 14.4 i) Result of comfort assessment steps criteria, through movements, observation, and scoring
2) A new redonning or repositioning does not constitute a fit test failure. Going with an
alternative respirator means the first one is excluded.

## Slide 57: Qualitative Respirator Fit Testing (QLFT)
Sensitivity screening test: The sensitivity screening test area shall be ventilated to prevent general room contamination with the challenge agent.
Fit testing shall be conducted so that it does not interfere with the sensitivity screening test.
Notes: As per slide

## Slide 58: Qualitative Respirator Fit Testing (QLFT)
Fit test exercises: The following exercises shall be performed while the person conducting the QLFT challenges the respirator seal with the test agent. Each exercise described shall be performed for at least 30 s:
normal breathing;
deep breathing. Be certain breaths are deep and regular;
turning head from side to side. Be certain movement is complete, within the test subject’s comfortable range of motion. Alert the test subject to inhale and exhale when the head is at either side and to avoid bumping on the shoulder;
nodding head up and down. Be certain that the test subject’s movements are complete, within a comfortable range of motion. Alert the test subject to inhale when the head is in the fully up position, to exhale when the head is in the fully down position, and to avoid bumping the respirator on the chest;
talking. Talk loud enough to be understood and slowly for the duration of this exercise. The person being tested should be instructed to count, recite the alphabet, talk about a subject that is relevant to work activities, or, if he/she prefers, read the “Rainbow Passage”
bending over, except where the test method will not permit it because of space limitations. The test subject bends at the waist and tries to keep the head and back parallel to the floor, repeating the movement at a comfortable pace and pausing long enough to inhale twice at each extreme position; and
g) normal breathing again.
Notes: As per slide

## Slide 59: Qualitative Fit Test (QLFT) Protocols - Saccharin
Saccharin taste threshold screening: The procedure shall be as follows:
The test subject shall not eat, drink (except plain water), smoke, or chew gum for 15 min before the test. Note: If the test subject eats or drinks something sweet before the screening test, he/she might be unable to taste the weak saccharin solution.
During threshold screening as well as during fit testing, subjects shall wear an enclosure about the head and shoulders that is approximately 300 mm (12 in) in diameter and 350 mm (14 in) tall. The front portion of the enclosure shall be clear from the respirator and allow free movement of the head when a respirator is worn.
The test enclosure shall have a 19 mm (3/4 in) hole in front of the test subject’s nose and mouth area to accommodate a nebulizer/atomizer nozzle.
The test subject shall don the test enclosure. Throughout the threshold screening test, the test subject shall breathe through his/her slightly open mouth with the tongue extended. The subject shall be instructed to report when he/she detects a sweet taste.
The threshold screening solution shall be prepared by dissolving 0.83 g (0.029 oz) of sodium saccharin USP in 100 mL (0.35 fl oz) of warm water or by putting 1 mL of the fit test solution in 100 mL (3.5 fl oz) of distilled water. Alternatively, a commercially available pre-mixed fit testing solution may be used
A small amount of the taste screening solution (~ 3 mL) (~ 0.01 fl oz) shall be added into a nebulizer. This nebulizer shall be clearly marked to distinguish it from the fit test solution nebulizer.
Using the nebulizer, the test conductor shall spray the threshold screening solution into the enclosure. The nozzle shall be directed away from the nose and mouth of the test subject.
To produce the aerosol, the nebulizer bulb shall be firmly squeezed so that it collapses completely, then released, and allowed to fully expand.
Ten squeezes shall be repeated rapidly and the test subject shall then be asked whether the saccharin can be tasted. If the test subject reports tasting the sweet taste during the ten squeezes, the screening test is complete. The taste threshold shall be noted as ten regardless of the number of squeezes actually completed.
If the first response is negative, ten more squeezes shall be repeated rapidly and the test subject shall again be asked whether the saccharin is tasted. If the test subject reports tasting the sweet taste during the second ten squeezes, the screening test is complete. The taste threshold shall be noted as 20 regardless of the number of squeezes actually completed.
If the second response is negative, ten more squeezes shall be repeated rapidly and the test subject shall again be asked whether the saccharin is tasted. If the test subject reports tasting the sweet taste during the third set of ten squeezes, the screening test is complete. The taste threshold shall be noted as 30 regardless of the number of squeezes actually completed.
The test conductor shall record the number of squeezes required to solicit a taste response.
If the saccharin is not tasted after 30 squeezes [see Item k)], the saccharin fit test shall not be used.
If a taste response is elicited, the test subject shall be asked to take note of the taste for reference in the fit test.
Correct use of the nebulizer means that approximately 1 mL (0.035 fl oz) of liquid is used at a time in the nebulizer body.
The nebulizer shall be thoroughly rinsed in water, shaken dry, and refilled at least each morning and periodically checked and maintained free of clogs.
Notes: The saccharin taste threshold screening, performed without using a respirator, is intended to determine whether the individual being tested can detect the taste of saccharin.

## Slide 60: Qualitative Fit Test (QLFT) Protocols - Saccharin
Saccharin solution aerosol QLFT protocol: The protocol for the saccharin solution aerosol QLFT shall be as follows:
The fit test shall use the same enclosure described in Clause B.3.2.2 b).
The test subject shall don the enclosure while using the selected respirator [see Clause B.2.2 d)]. The respirator shall be properly adjusted and equipped with a particulate filter(s).
A second nebulizer/atomizer shall be used to spray the fit test solution into the enclosure. This nebulizer shall be clearly marked to distinguish it from the screening test solution nebulizer.
The fit test solution shall be prepared by adding 83 g (0.029 oz) of sodium saccharin USP to 100 mL (3.5 fl oz) of warm water. Alternatively, a commercially available premixed fit testing solution may be used.
A small amount of the fit test solution (~ 3 mL) (~ 0.01 fl oz) shall be added into the nebulizer
As before, the test subject shall breathe through a slightly open mouth with tongue extended and report if he/she tastes the sweet taste of saccharin.
The nebulizer shall be inserted into the hole in the front of the enclosure and an initial concentration of saccharin fit test solution shall be sprayed into the enclosure using the same number of squeezes (either 10, 20, or 30 squeezes) required to elicit a taste response as noted during the screening test. A minimum of ten squeezes is required.
After the aerosol has been generated, the test subject shall be instructed to perform the exercises described in Clause B.2.5.2.
Every 30 s the aerosol concentration shall be replenished using one-half the number of squeezes recorded initially (i.e., 5, 10, or 15).
The test subject shall indicate to the test conductor if at any time during the fit test the taste of saccharin is detected. If the taste of saccharin is detected, the fit shall be deemed unsatisfactory and the test has failed. A different respirator shall be tried and the entire test procedure shall be repeated (taste threshold screening and fit testing).
If the test subject does not report tasting the saccharin, the test has passed.
Prior to removing the enclosure following a satisfactory fit test, the test conductor shall ask the test subject to break the face-to-facepiece seal. Having the test subject detect the test agent confirms the validity of the fit test and the effectiveness of the respirator.
The test conductor shall make periodic checks of the nebulizer to ensure that it is not clogged. If clogging is found at the end of the test session, the test shall be deemed invalid and shall be repeated.
Notes: As per slide

## Slide 61: Qualitative Fit Test (QLFT) Protocols – Bitter aerosol
Bitter aerosol taste threshold screening: The bitter aerosol taste threshold screening, performed without using a respirator, is intended to determine whether the individual being tested can detect the taste of bitter aerosol.
The screening method shall be as follows:
The test subject shall not eat, drink (except plain water), smoke, or chew gum for 15 min before the test is conducted.
The fit test shall use the same enclosure as that described in Clause B.3.2.2 b).
The test enclosure shall have a 19 mm (3/4 in) hole in front of the test subject’s nose and mouth area to accommodate a nebulizer/atomizer nozzle.
The test subject shall don the test enclosure. Throughout the threshold screening test, the test subject shall breathe through his/her slightly open mouth with the tongue extended. The subject is instructed to report when he/she detects a bitter taste
The threshold screening solution shall be prepared by adding 13.5 mg (0.0005 oz) of bitter aerosol to 100 mL (3.5 fl oz)of 5% salt (NaCl) by weight solution in distilled water. Alternatively, a commercially available pre-mixed fit testing solution may be used.
A small amount of the taste screening solution (~ 3 mL) (~ 0.01 fl oz) shall be added into a nebulizer. This nebulizer shall be clearly marked to distinguish it from the fit test solution nebulizer.
Using the nebulizer, the test conductor shall spray the threshold check solution into the enclosure.
To produce the aerosol, the nebulizer bulb shall be firmly squeezed so that the bulb collapses completely, then released, and allowed to fully expand.
An initial ten squeezes shall be repeated rapidly and the test subject shall then be asked whether the bitter aerosol can be tasted. If the test subject reports tasting the bitter taste during the ten squeezes, the screening test is complete. The taste threshold shall be noted as ten regardless of the number of squeezes actually completed.
If the first response is negative, ten more squeezes shall be repeated rapidly and the test subject shall again be asked whether the bitter aerosol is tasted. If the test subject reports tasting the bitter taste during the second ten squeezes, the screening test is complete. The taste threshold shall be noted as 20 regardless of the number of squeezes actually completed.
If the second response is negative, ten more squeezes shall be repeated rapidly and the test subject shall again be asked whether the bitter aerosol is tasted. If the test subject reports tasting the bitter taste during the third set of ten squeezes, the screening test is complete. The taste threshold shall be noted as 30 regardless of the number of squeezes actually completed.
The test conductor shall take note of the number of squeezes required to solicit a taste response.
If the bitter aerosol is not tasted after 30 squeezes [see Item k)], the test subject is unable to taste bitter aerosol and the bitter aerosol fit test shall not be used.
If a taste response is elicited, the test subject shall be asked to take note of the taste for reference in the fit test.
Correct use of the nebulizer means that approximately 1 mL (0.035 fl oz) of liquid is used at a time in the nebulizer body.
The nebulizer shall be thoroughly rinsed in water, shaken to dry, and refilled at least each morning and afternoon or at least every 4 h.
Notes: As per slide

## Slide 62: Qualitative Fit Test (QLFT) Protocols – Bitter Aerosol
Bitter aerosol QLFT protocol: The protocol for the bitter aerosol QLFT shall be as follows:
The test subject shall not eat, drink (except plain water), smoke, or chew gum for 15 min before the test.
The fit test shall use the same enclosure as that described in Clause B.3.2.2 b).
The test subject shall don the enclosure while using the selected respirator [see Clause B.2.2 d)]. The respirator shall be properly adjusted and equipped with any type of particulate filter.
A second nebulizer/atomizer shall be used to spray the fit test solution into the enclosure. This nebulizer shall be clearly marked to distinguish it from the screening test solution nebulizer. Respiratory Protection Program Fit Tester Protocols and Resources SASWH - May 1, 2020 r: Apr2021 Page 30.
The fit test solution shall be prepared by adding 337.5 mg (0.0125 oz) of bitter aerosol to 200 mL (7.0 fl oz) of a 5% salt (NaCl) solution in warm water. Alternatively, a commercially available pre- mixed fit testing solution may be used.
A small amount of the fit test solution (~ 3 mL) (~ 0.01 fl oz) shall be added into the nebulizer.
As before, the test subject shall breathe through his/her slightly open mouth with tongue extended and be instructed to report if he/she tastes the bitter aerosol.
The nebulizer shall be inserted into the hole in the front of the enclosure and an initial concentration of the fit test solution shall be sprayed into the enclosure using the same number of squeezes (either 10, 20, or 30 squeezes) required to elicit a taste response as noted during the screening test.
After the aerosol is generated, the test subject shall be instructed to perform the exercises described in Clause B.2.5.2.
Every 30 s the aerosol concentration shall be replenished using one half the number of squeezes used initially (i.e., 5, 10, or 15).
The test subject shall indicate to the test conductor if at any time during the fit test the taste of bitter aerosol is detected. If the test subject does not report tasting the bitter aerosol, the test has passed.
If the taste of bitter aerosol is detected, the fit shall be deemed unsatisfactory and the test has failed. A different respirator shall be tried and the entire test procedure repeated (taste threshold screening and fit testing).
Prior to removing the enclosure following a satisfactory fit test, the test conductor shall ask the test subject to break the face-to-facepiece seal. Having the test subject detect the test agent confirms the validity of the fit test and the effectiveness of the respirator.
Notes: As per slide

## Slide 63: Quantitative respirator fit tests (QNFT)
Introduction of QNFT to respirator users: The person conducting the QNFT shall provide the test subject with an introduction to QNFT. In this introduction, the fit tester shall
explain what the QNFT procedure is, why it is required, and the importance of using a respirator that provides an effective, reproducible face-to-facepiece seal;
explain why the test is important, in order to convince the test subject to co-operate fully in the QNFT;
describe the challenge agent (e.g., ambient dust, generated aerosol, negative pressure) used in the QNFT;
describe how the test subject selects a properly fitting and comfortable respirator from those that are appropriate to the application;
explain that the respirator is equipped with the appropriate adapters or filters for the QNFT being used;
explain that the test subject is required to successfully complete the positive- or negative-pressure user seal check with the selected respirator without physical or verbal assistance prior to proceeding with the QNFT;
explain that the test subject is required to don the respirator properly, without physical or verbal assistance, in accordance with the manufacturer’s instructions;
explain that the test subject is required, during the QNFT, to wear other PPE that he/she could be required to use in the workplace and that could affect the face-to-facepiece seal;
describe the QNFT exercises and how to perform them during the QNFT;
explain why it is important to use, in the workplace, the specific brand, model, and size of facepiece that is used to pass the QNFT; and
emphasize that the user must always inspect a respirator before using it to ensure that it is in proper working condition
Notes: As per slide

## Slide 64: Donning and Doffing
Notes: Demonstrate how to Don and Doff 3M1860
If unsure how to don and doff – refer to box and/or package insert
Have participants perform a return demonstration

## Slide 65: Donning and Doffing
Notes: Demonstrate how to Don and doff 3m1870+
If unsure how to don and doff – refer to box and/or package insert
Have participants perform a return demonstration

## Slide 66: Donning and Doffing
Notes: Demonstrate how to don and doff 3M1804 vlfex
If unsure how to don and doff – refer to box and/or package insert
Have participants perform a return demonstration

## Slide 67: Donning and Doffing
Notes: Demonstrate how to don and doff a halyard
If unsure how to don and doff – refer to box and/or package insert
Have participants perform a return demonstration

## Slide 68: Donning and Doffing
Notes: Demonstrate how to don and doff 3M8210
If unsure how to don and doff – refer to box and/or package insert
Have participants perform a return demonstration

## Slide 69: Donning and Doffing
Notes: Demonstrate how to don and doff elastomeric
If unsure how to don and doff – refer to box and/or package insert

## Slide 70: Forms
Orientation
Screening form
Documentation form
Notes: Go through orientation in detail, screening form in detail, and documentation form in detail.

## Slide 71: Set up and Practice QLFT
Notes: Set up and conduct sensitivity – have participants perform a return demonstration using proper paper work
Set up QLT station and demonstrate – have participants perform a return demonstration using proper paperwork

## Slide 72: Set up and practice QNFT
Notes: IF not teaching QNFT hide slide.
If teaching QNFT demonstrate equipment set up, perform a fit test and have participants perform a return demonstration.

## Slide 73: Congratulations
You are now a qualified fit tester!!!
You will receive a wallet card, and will be required to recertify in two years
Notes: As per slide